## Slide 1
OpenUSD · PR 105 · applied to AAS
Pointing OpenUSD at the Asset Administration Shell
A source-identifier hello-world
Applied demonstration of Separation of Concerns for Identifiers (PR 105)

## Slide 2
The idea
▍ A USD prim carries one thing — a stable globalAssetId.
  No copied data. No network endpoints. Just durable identity, in USD's existing assetInfo.
▍ At runtime, a consumer resolves the live AAS data and does real work with it.
  Reads the id off the prim → resolves over the standard AAS APIs → rolls up a Product Carbon Footprint.
▍ The data is never mirrored into the scene.
  USD stays a portable description of what the asset is; the AAS stays the authoritative source of its data.

## Slide 3
Why it matters — and why the obvious ways break
Industrial digital twins aggregate thousands of vendor components — each with authoritative data in a system of record.
▍ Copy the data into the scene → it goes stale.
  An aggregate built from copied data can't be trusted: a missing value looks identical to a zero.
▍ Bake the source endpoints into the scene → it goes brittle.
  Can't move site-to-site or stage-to-stage without rewiring; one asset with several shells has nowhere to put them.
▍ AAS is the open standard for industrial asset data.
  Stable globalAssetId per shell; submodels for Nameplate, Technical Data, Carbon Footprint, and more.

## Slide 4
Two concerns, separated — the PR 105 idea
▍ Concern 1 — External ID'ing. “Which external entity is this prim?”
  assetInfo.sourceIds.aas = { globalAssetId } — provenance only, no endpoints in USD.
▍ Concern 2 — Data binding / resolution. “What data attaches, and how?”
  An injected resolver: discovery / registry / repository clients fetch submodels on demand.
▍ Independent and individually optional.
  Identity travels with the asset; resolution is supplied by the consumer, wherever it runs. That is what keeps the scene portable.

## Slide 5
Architecture · 1 — identity-only USD
The entire asset on the USD side — no endpoints, no copied submodels:
def Xform "IESEDriveMotorDM3000" (
assetInfo = {
dictionary sourceIds = {
dictionary aas = {
string globalAssetId = "urn:fraunhofer:iese:...:serial-0042"
}
}
}
) { }
USD's existing assetInfo metadata — no new schema required, ships today.

## Slide 6
Architecture · 2 — runtime-injected resolve
One seam takes the stable identity + a context, and walks the standard AAS chain with failover:
def resolve(global_asset_id, context) -> ResolvedAsset:
# Hop 1 Discovery: globalAssetId -> [aasId, ...]
# Hop 2 Registry: aasId -> repository endpoint
# Hop 3 Repository: fetch shell; submodels fetched lazily
...
Endpoints live in the context, supplied at runtime — never in USD. Same id resolves to different shells in different contexts. Lazy fetch: cost scales with what's accessed; result is read-once, cacheable.

## Slide 7
Architecture · 3 — used, not mirrored
▍ The consumer does its work with the live data — and does not write it back into USD.
  Binding-pointer posture (PR 105): USD carries the identifier, the AAS holds the data, the consumer pulls on demand.
▍ Mirroring AAS submodels into USD attributes would re-create the staleness problem.
  It duplicates the source-of-record schema into the scene — exactly what the architecture avoids.
▍ Terminology note: this resolve() is not USD value/asset resolution.
  It's the AAS data-acquisition step (globalAssetId -> live data over HTTP). The name is kept for continuity.

## Slide 8
What runs today
End to end against Eclipse BaSyx + its public Fraunhofer-IESE drivemotor shell:
EN 15804 stage | kg CO₂e / piece
A1 — raw materials | 180
A2 — transport | 25
A3 — manufacturing | 80
Cradle-to-gate (A1–A3) | 285 ✓ complete
Use (B*), end-of-life (C*) | not reported — flagged
CarbonFootprint submodel (IDTA 02023); fields located by semanticId, robust to idShort variation. Nothing written back into USD — the roll-up is computed in the consumer.

## Slide 9
Why gap-flagging is the point
▍ A report-grade roll-up must tell “footprint is zero” apart from “never reported a footprint.”
  Coverage is a first-class output: sum only the stages reported; name what's missing.
▍ A missing value is never silently coerced to zero.
  Missing PCF, missing CO₂e, incomplete cradle-to-gate, unreported use phase — each is flagged.
▍ Gaps are actionable — they tell you which supplier to chase.
  The roll-up sums across components, so it extends directly to a bill of materials.

## Slide 10
Roadmap & references
▍ Bill-of-materials roll-up (next): several components, one scene, carbon rolled up across the assembly, gaps named.
▍ Change-driven refresh (later): identity and fetch are decoupled, so push-refresh drops in when AAS notifications mature.
▍ Read-once today proves the binding; push-refresh follows when the source side is ready.
References
PR 105 — Separation of Concerns for Identifiers · github.com/PixarAnimationStudios/OpenUSD-proposals/pull/105
AAS DPP ↔ OpenUSD PoC (M. Wagner, SyncTwin) · github.com/asluk/OpenUSD-proposals/pull/2
AAS specifications (IDTA) · industrialdigitaltwin.org · Eclipse BaSyx · github.com/eclipse-basyx
Omniverse DSX Blueprint (domain motivation) · blogs.nvidia.com/blog/omniverse-dsx-blueprint